CNT_DAC_TB
library ieee;
use ieee.std_logic_1164.all;

entity cnt_dac_tb is
end entity cnt_dac_tb;

architecture for_dac_tb of cnt_dac_tb is

  signal CLK : std_logic := '1';
  signal RST : std_logic;
  signal DATO1 : std_logic_vector(7 downto 0);
  signal DATO2 : std_logic_vector(7 downto 0);
  signal DATO_OK : std_logic;
  signal SYNC : std_logic;
  signal SCLK : std_logic;
  signal D1 : std_logic;
  signal D2 : std_logic;

begin -- architecture for_dac_tb

  DUT : entity work.cnt_dac
    port map (
      CLK => CLK,
      RST => RST,
      DATO1 => DATO1,
      DATO2 => DATO2,
      DATO_OK => DATO_OK,
      SYNC => SYNC,
      SCLK => SCLK,
      D1 => D1,
      D2 => D2);

  T1 : entity work.DAC121S101
    port map (
    SYNC => SYNC,
    SCLK => SCLK,
    DIN => D1);

  T2 : entity work.DAC121S101
    port map (
    SYNC => SYNC,
    SCLK => SCLK,
    DIN => D2);

  -- clock generation
  Clk <= not Clk after 5 ns;
  rst <= '1', '0' after 50 ns;
  DATO1 <= x"00", x"A5" after 100 ns;
  DATO2 <= x"00", x"5A" after 120 ns;
  DATO_OK <= '0', '1' after 200 ns, '0' after 220 ns;
end architecture for_dac_tb;