CNT_DPRAM_TB
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;

-------------------------------------------------------------------------------

entity cnt_dpram_tb is

end entity cnt_dpram_tb;

-------------------------------------------------------------------------------

architecture cnt_dpram of cnt_dpram_tb is

  -- component ports
  signal CLK : std_logic := '1' ;
  signal RST : std_logic;
  signal DIR : std_logic_vector (7 downto 0):= (others => '0');
  signal DIR_VLD : std_logic :='0';
  signal DATO : std_logic_vector (7 downto 0):= (others => '0');
  signal DATO_VLD : std_logic :='0';
  signal ADDRESS : std_logic_vector(7 downto 0);
  signal DATA : std_logic_vector(7 downto 0);
  signal WE_DP1 : std_logic;
  signal WE_DP2 : std_logic;

begin -- architecture cnt_dpram

  -- component instantiation
  DUT: entity work.cnt_dpram
    port map (
      CLK => CLK,
      RST => RST,
      DIR => DIR,
      DIR_VLD => DIR_VLD,
      DATO => DATO,
      DATO_VLD => DATO_VLD,
      ADDRESS => ADDRESS,
      DATA => DATA,
      WE_DP1 => WE_DP1,
      WE_DP2 => WE_DP2);

  -- clock generation
  CLK <= not CLK after 5 ns;
  RST <= '1', '0' after 50 ns;

  process is

    procedure dpram(Dvalue:in std_logic_vector(7 downto 0);
        Dat:in integer;
        Daux:in integer)is
      begin
        wait for 60 ns;
        DIR <= Dvalue;
        DIR_VLD <= '1';
        wait for 10 ns;
        DIR_VLD <= '0';
        wait for 40 ns;
        DATO <= std_logic_vector(to_unsigned(Dat+Daux, 8));
        DATO_VLD <= '1';
        wait for 10 ns;
        DATO_VLD <= '0';
      end procedure;

  begin
    wait for 100 ns;
    for io in 0 to 5 loop
      dpram(Dvalue => x"A1",Dat => 35,Daux => io);
    end loop;
    for iu in 0 to 10 loop
      dpram(Dvalue => x"A2",Dat => 213,Daux => iu);
    end loop;
    dpram(Dvalue => x"AA",Dat => 73,Daux => 0);
    for ie in 0 to 2 loop
      dpram(Dvalue => x"A2",Dat => 11,Daux => ie);
    end loop;
    dpram(Dvalue => x"AA",Dat => 30,Daux => 1);
    for ia in 0 to 2 loop
      dpram(Dvalue => x"A1",Dat => 251,Daux => ia);
    wait for 60 ns;
    end loop;
    assert True report "FINAL TEST" severity note;
  end process;

end architecture cnt_dpram;