DCM
library ieee;
use ieee.std_logic_1164.all;
use ieee.std_logic_unsigned.all;
use ieee.std_logic_arith.all;
use ieee.numeric_std.all;

library unisim;
use unisim.vcomponents.all;

entity dcm is
port
 (-- Clock in ports
  CLK_IN : in std_logic;
  -- Clock out ports
  CLK_OUT : out std_logic;
  -- Status and control signals
  RESET : in std_logic
 );
end dcm;

architecture xilinx of dcm is
  attribute CORE_GENERATION_INFO : string;
  attribute CORE_GENERATION_INFO of xilinx :
  -- Input clock buffering / unused connectors
  signal clkin1 : std_logic;
  -- Output clock buffering
  signal clk_out1_internal : std_logic;
  signal clkfb : std_logic;
  signal clk0 : std_logic;
  signal clkfbout : std_logic;
  signal locked_internal : std_logic;
  signal status_internal : std_logic_vector(7 downto 0);
begin

  -- Input buffering
  --------------------------------------
  clkin1_buf : IBUFG
  port map
   (O => clkin1,
    I => CLK_IN);

  -- Clocking primitive
  --------------------------------------

  -- Instantiation of the DCM primitive
  -- * Unused inputs are tied off
  -- * Unused outputs are labeled unused
  dcm_sp_inst: DCM_SP
  generic map
   (CLKDV_DIVIDE => 2.000,
    CLKFX_DIVIDE => 1,
    CLKFX_MULTIPLY => 4,
    CLKIN_DIVIDE_BY_2 => FALSE,
    CLKIN_PERIOD => 10.0,
    CLKOUT_PHASE_SHIFT => "NONE",
    CLK_FEEDBACK => "1X",
    DESKEW_ADJUST => "SYSTEM_SYNCHRONOUS",
    PHASE_SHIFT => 0,
    STARTUP_WAIT => FALSE)
  port map
   -- Input clock
   (CLKIN => clkin1,
    CLKFB => clkfb,
    -- Output clocks
    CLK0 => clk0,
    CLK90 => open,
    CLK180 => open,
    CLK270 => open,
    CLK2X => open,
    CLK2X180 => open,
    CLKFX => open,
    CLKFX180 => open,
    CLKDV => open,
   -- Ports for dynamic phase shift
    PSCLK => '0',
    PSEN => '0',
    PSINCDEC => '0',
    PSDONE => open,
   -- Other control and status signals
    LOCKED => locked_internal,
    STATUS => status_internal,
    RST => RESET,
   -- Unused pin, tie low
    DSSEN => '0');

  -- Output buffering
  -------------------------------------
  clkfb <= clk_out1_internal;

  clkout1_buf : BUFG
  port map
   (O => clk_out1_internal,
    I => clk0);

  CLK_OUT <= clk_out1_internal;

end xilinx;