DPRAM_MEM_TB
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;

entity dpram_mem_tb is
end entity dpram_mem_tb;

architecture dpram_mem of dpram_mem_tb is

  -- component ports
  signal DIN : std_logic_vector(7 downto 0) :=(others =>'0');
  signal ADDR_IN : std_logic_vector(7 downto 0) :=(others =>'0');
  signal WE : std_logic:='0';
  signal CLK : std_logic:='1' ;
  signal RST : std_logic;
  signal ADDR_OUT : std_logic_vector(7 downto 0) :=(others =>'0');
  signal DOUT : std_logic_vector(7 downto 0);

begin -- architecture dpram_mem

  DUT: entity work.dpram_mem
    port map (
      DIN => DIN,
      ADDR_IN => ADDR_IN,
      WE => WE,
      CLK => CLK,
      RST => RST,
      ADDR_OUT => ADDR_OUT,
      DOUT => DOUT);

  CLK <= not CLK after 5 ns;
  RST <= '1', '0' after 50 ns;

  process is
  begin -- process escritura
    wait for 100 ns;
    for i in 0 to 255 loop
      DIN <= std_logic_vector(to_unsigned(35+i, 8));
      ADDR_IN <= std_logic_vector(to_unsigned(i, 8));
      WE <= '1';
      wait for 10 ns;
      WE <= '0';
      wait for 10 ns;
    end loop; -- i
  end process;

  process is
  begin -- process lectura
    wait for 200 ns;
    for o in 0 to 255 loop
      ADDR_OUT <= std_logic_vector(to_unsigned(o, 8));
      wait for 20 ns;
    end loop; -- o
  end process;

end architecture dpram_mem;