EPP_DEVICE
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
use std.textio.all;
use ieee.std_logic_textio.all;

entity epp_device is
  port (
    DATA : inout std_logic_vector(7 downto 0);
    PWRITE : out std_logic;
    DSTRB : out std_logic;
    ASTRB : out std_logic;
    PWAIT : in std_logic);

end epp_device;
architecture sim of epp_device is
  constant T_clk_epp : time := 100 ns; -- Internal clock period.
  signal clk_epp : std_logic := '0'; -- Internal clock signal.
  signal read_value : std_logic_vector(7 downto 0) := (others => '0');
  constant dir_frec : std_logic_vector(7 downto 0) := x"F0";
  constant dir_dpram1 : std_logic_vector(7 downto 0) := x"A1";
  constant dir_dpram2 : std_logic_vector(7 downto 0) := x"A2";
  constant EPP_cicle_length : natural := 10;
begin
  -- internal clock signal generation.

  clk_epp <= not(clk_epp) after T_clk_epp/2;

  process
    procedure epp_cicle (address : in std_logic_vector(7 downto 0);
        data_io : inout std_logic_vector(7 downto 0);
        r_w : in character) is

    begin
      wait until clk_epp = '1';
      PWRITE <= '0';
      wait until clk_epp = '1';
      ASTRB <= '0';
      data <= address;
      wait for T_clk_epp*EPP_cicle_length;
      ASTRB <= '1';
      wait until clk_epp = '1';
      data <= (others => 'Z');
      PWRITE <= '1';
      wait until clk_epp = '1';
      wait for T_clk_epp*EPP_cicle_length;
-------------------------------------------------------------------------------
      if r_w = 'w' then -- write cicle
        PWRITE <= '0';
        data <= data_io;
      end if;
-------------------------------------------------------------------------------
      wait until clk_epp = '1';
      DSTRB <= '0';
      wait for T_clk_epp*EPP_cicle_length;
      if r_w = 'r' then
        data_io := data;
      end if;

      DSTRB <= '1';
      wait until clk_epp = '1';
      data <= (others => 'Z');
      PWRITE <= '1';
      wait until clk_epp = '1';

    end procedure;

    file arch_in : text;
    variable bf : line;
    variable dato : std_logic_vector(7 downto 0);
    variable dir : std_logic_vector(7 downto 0);
  begin
    --inicialización
    data <= (others => 'Z');
    PWRITE <= '1';
    DSTRB <= '1';
    ASTRB <= '1';
    dir := (others => '0');
    wait for 130 ns;
    DIR := dir_dpram1;
    DATO := X"34";
    epp_cicle (address => dir,
        data_io => dato,
        r_w => 'w');

    DIR := x"32";
    epp_cicle (address => dir,
        data_io => dato,
        r_w => 'r');

    read_value <= dato;

wait for 130 ns;
    DIR := dir_frec;
    DATO := X"22";
    epp_cicle (address => dir,
        data_io => dato,
        r_w => 'w');

wait for 130 ns;

    DIR := dir_dpram2;
    DATO := X"11";
    epp_cicle (address => dir,
        data_io => dato,
        r_w => 'w');

    wait for 1 us;

    report "FIN CICLO R/W" severity failure;

  end process;
end sim;