EPP_DEVICE 1
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
use std.textio.all;
use ieee.std_logic_textio.all;

entity epp_device1 is
  port (
    DATA : inout std_logic_vector(7 downto 0);
    PWRITE : out std_logic;
    DSTRB : out std_logic;
    ASTRB : out std_logic;
    PWAIT : in std_logic);

end epp_device1;
architecture sim of epp_device1 is
  constant T_clk_epp : time := 100 ns; -- Internal clock period.
  signal clk_epp : std_logic := '0'; -- Internal clock signal.
  signal read_value : std_logic_vector(7 downto 0) := (others => '0');
  constant dir_frec : std_logic_vector( 7 downto 0) := x"F0";
  constant dir_dpram1 : std_logic_vector( 7 downto 0) := x"A1";
  constant dir_dpram2 : std_logic_vector( 7 downto 0) := x"A2";
  constant EPP_cicle_length : real := 0.5;
begin
  -- internal clock signal generation.

  clk_epp <= not(clk_epp) after T_clk_epp/2;

 process

    procedure epp_cicle ( address : in std_logic_vector(7 downto 0);
        data_io : inout std_logic_vector(7 downto 0);
        r_w : in character) is

    begin
      wait until clk_epp = '1';
      PWRITE <= '0';
      wait until clk_epp = '1';
      ASTRB <= '0';
      data <= address;
      wait for T_clk_epp*EPP_cicle_length;
      ASTRB <= '1';
      wait until clk_epp = '1';
      data <= (others => 'Z');
      PWRITE <= '1';
      wait until clk_epp = '1';
      wait for T_clk_epp*EPP_cicle_length;
-------------------------------------------------------------------------------
      if r_w = 'w' then -- write cicle
        PWRITE <= '0';
        data <= data_io;
      end if;
-------------------------------------------------------------------------------
      wait until clk_epp = '1';
      DSTRB <= '0';
      wait for T_clk_epp*EPP_cicle_length;
      if r_w = 'r' then
        data_io:= data;
      end if;

      DSTRB <= '1';
      wait until clk_epp = '1';
      data <= (others => 'Z');
      PWRITE <= '1';
      wait until clk_epp = '1';

    end procedure;

file arch_in : text ;
 variable bf : line;
    variable dato_rd : std_logic_vector(7 downto 0);
     variable dato : std_logic_vector(7 downto 0);
    variable dir : std_logic_vector(7 downto 0);
  begin
    --inicialización
    data <= (others => 'Z');
    PWRITE <= '1';
    DSTRB <= '1';
    ASTRB <= '1';
    dir := (others => '0');
    wait for 160 ns;

    file_open(arch_in,"../Souce/Vo1.dat",read_mode);
     dir:= dir_dpram1 ;
    while not endfile(arch_in) loop
      readline (arch_in, bf);
      hread (bf, dato_rd);
      dato:=dato_rd;
      epp_cicle ( address => dir,
        data_io => dato,
        r_w => 'w');

    end loop;
    file_close(arch_in);

 file_open(arch_in,"../Souce/Vo2.dat",read_mode);
    dir:= dir_dpram2 ;

    while not endfile(arch_in) loop
      readline (arch_in, bf);
      hread (bf, dato_rd);
      dato:=dato_rd;
      epp_cicle ( address => dir,
        data_io => dato,
        r_w => 'w');
    end loop;
    file_close(arch_in);

    dir := dir_frec ;
dato:=x"13";
    epp_cicle ( address => dir,
        data_io => dato,
        r_w => 'w');

wait for 5 ms;

    dir := dir_frec ;
dato:=x"73";
    epp_cicle ( address => dir,
        data_io => dato,
        r_w => 'w');

wait for 5 ms;

    dato:=x"bf";
    epp_cicle ( address => dir,
        data_io => dato,
        r_w => 'w');

    wait for 5 ms;

    dato:=x"ff";
    epp_cicle ( address => dir,
        data_io => dato,
        r_w => 'w');

wait for 5 ms;
   report "FIN CONTROLADO DE LA SIMULACION" severity failure;
  end process;
end sim;