GEN_DIR_TB
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;

-------------------------------------------------------------------------------

entity gen_dir_tb is

end entity gen_dir_tb;

-------------------------------------------------------------------------------

architecture gen_dir of gen_dir_tb is

  -- component ports
  signal CLK : std_logic := '0';
  signal RST : std_logic := '1';
  signal DIR : std_logic_vector (7 downto 0) := (others => '0');
  signal DIR_VLD : std_logic := '0';
  signal DATO : std_logic_vector (7 downto 0) := (others => '0');
  signal DATO_VLD : std_logic := '0';
  signal ADDR_OUT : std_logic_vector(7 downto 0);
  signal DATO_OK : std_logic;

begin -- architecture gen_dir

  -- component instantiation
  DUT : entity work.gen_dir
    port map (
      CLK => CLK,
      RST => RST,
      DIR => DIR,
      DIR_VLD => DIR_VLD,
      DATO => DATO,
      DATO_VLD => DATO_VLD,
      ADDR_OUT => ADDR_OUT,
      DATO_OK => DATO_OK);

  -- clock generation
  CLK <= not CLK after 5 ns;
  RST <= '1', '0' after 30 ns;

  process is

    procedure dpram(Dvalue:in std_logic_vector(7 downto 0);
        Dat:in std_logic_vector(7 downto 0))is
      begin
        DIR <= Dvalue;
        DIR_VLD <= '1';
        wait for 10 ns;
        DIR_VLD <= '0';
        wait for 50 ns;
        DATO <= Dat;
        DATO_VLD <= '1';
        wait for 10 ns;
        DATO_VLD <= '0';
      end procedure;

  begin
    wait for 80 ns;
    dpram(Dvalue => x"FF",Dat => x"0A");
wait for 1000 ns;
    dpram(Dvalue => x"F0",Dat => x"0A");
wait for 50000 ns;
    dpram(Dvalue => x"FF",Dat => x"0A");
wait for 2000 ns;
    assert True report "FINAL TEST" severity note;
  end process;

end architecture gen_dir;