GEN_FUNCIONES
library ieee;
use ieee.std_logic_1164.all;

entity gen_funciones is
  port (
    RELOJ : in std_logic;
    RST : in std_logic;
    ASTRB : in std_logic;
    DSTRB : in std_logic;
    DATA : inout std_logic_vector(7 downto 0);
    PWRITE : in std_logic;
    PWAIT : out std_logic;
    SYNC : out std_logic;
    SCLK : out std_logic;
    D1 : out std_logic;
    D2 : out std_logic);
end gen_funciones;

architecture rtl of gen_funciones is

  signal CLK : std_logic;
  signal DIR : std_logic_vector (7 downto 0);
  signal DIR_VLD : std_logic;
  signal DATO : std_logic_vector (7 downto 0);
  signal DATO_VLD : std_logic;
  signal DATO_RD : std_logic_vector (7 downto 0);
  signal CE_RD : std_logic;
 signal ADDRESS : std_logic_vector(7 downto 0);
  signal DATA_DP : std_logic_vector (7 downto 0);
  signal WE_DP1 : std_logic;
  signal WE_DP2 : std_logic;
  signal DATO1 : std_logic_vector (7 downto 0);
  signal DATO2 : std_logic_vector (7 downto 0);
  signal ADDR_OUT : std_logic_vector(7 downto 0);
  signal DATO_OK : std_logic;
begin -- rtl

U_dcm :entity work.dcm
  port map
   (CLK_IN => RELOJ,
    CLK_OUT => CLK,
    RESET => RST);

 U_cnt_epp:entity work.cnt_epp
    port map (
        CLK => CLK,
        RST => RST,
        ASTRB => ASTRB,
        DSTRB => DSTRB,
        DATA => DATA,
        PWRITE => PWRITE,
        PWAIT => PWAIT,
        DATO_RD => DATO_RD,
        CE_RD => CE_RD,
        DIR => DIR,
        DIR_VLD => DIR_VLD,
        DATO => DATO,
        DATO_VLD => DATO_VLD);

 U_cnt_dpram:entity work.cnt_dpram
    port map (
        CLK => CLK,
        RST => RST,
        DIR => DIR,
        DIR_VLD => DIR_VLD,
        DATO => DATO,
        DATO_VLD => DATO_VLD,
        ADDRESS => ADDRESS,
        DATA => DATA_DP,
        WE_DP1 => WE_DP1,
        WE_DP2 => WE_DP2);

  U_dpram_mem1 : entity work.dpram_mem
    port map (
        DIN => DATA_DP,
        ADDR_IN => ADDRESS,
        WE => WE_DP1,
        CLK => CLK,
        RST => RST,
        ADDR_OUT => ADDR_OUT,
        DOUT => DATO1);

  U_dpram_mem2 : entity work.dpram_mem
    port map (
        DIN => DATA_DP,
        ADDR_IN => ADDRESS,
        WE => WE_DP2,
        CLK => CLK,
        RST => RST,
        ADDR_OUT => ADDR_OUT,
        DOUT => DATO2);

   U_gen_dir:entity work.gen_dir
    port map (
        CLK => CLK,
        RST => RST,
        DIR => DIR,
        DIR_VLD => DIR_VLD,
        DATO => DATO,
        DATO_VLD => DATO_VLD,
        ADDR_OUT => ADDR_OUT,
        DATO_OK => DATO_OK);

  U_cnt_dac :entity work.cnt_dac
    port map (
      CLK => CLK,
      RST => RST,
      DATO1 => DATO1,
      DATO2 => DATO2,
      DATO_OK => DATO_OK,
      SYNC => SYNC,
      SCLK => SCLK,
      D1 => D1,
      D2 => D2);

end rtl;