TOP_SYSTEM 1
library ieee;
use ieee.std_logic_1164.all;

entity top_system1 is
  port(
    CLK : in std_logic;
    RST : in std_logic;
    ASTRB : in std_logic;
    DSTRB : in std_logic;
    DATA : inout std_logic_vector(7 downto 0);
    PWRITE : in std_logic;
    PWAIT : out std_logic;
    SWITCHES_I : in std_logic_vector(7 downto 0);
    PSH_BUTTON : in std_logic;
    LEDS_O : out std_logic_vector (7 downto 0));
end top_system1;

architecture rtl of top_system1 is
  signal DIR ,DIR_REG, DATO, DATO_REG, DATO_RD : std_logic_vector (7 downto 0);
  signal DIR_VLD, DATO_VLD, CE_RD : std_logic;
begin -- rtl

  DUT : entity work.cnt_epp
    port map (
      CLK => CLK,
      RST => RST,
      ASTRB => ASTRB,
      DSTRB => DSTRB,
      DATA => DATA,
      PWRITE => PWRITE,
      PWAIT => PWAIT,
      DATO_RD => DATO_RD,
      CE_RD => CE_RD,
      DIR => DIR,
      DIR_VLD => DIR_VLD,
      DATO => DATO,
      DATO_VLD => DATO_VLD);

  process (CLK, RST)
  begin
   if RST='0' then
      DIR_REG <= (others => '0');
   elsif (CLK'event and CLK='1') then
      if DIR_VLD = '1' then
        DIR_REG <= DIR;
      end if;
   end if;
  end process;

  process (CLK, RST)
  begin
   if RST='0' then
      DATO_REG <= (others => '0');
   elsif (CLK'event and CLK='1') then
      if DATO_VLD = '1' then
        DATO_REG <= DATO;
      end if;
   end if;
  end process;

 LEDS_O <= DATO_REG WHEN PSH_BUTTON ='1' ELSE DIR_REG;

   process (DIR, CE_RD, SWITCHES_I) is
   begin
    if DIR=x"32" and CE_RD='1' then
      DATO_RD <= SWITCHES_I;
    else
      DATO_RD <= (others => '0');
    end if;
   end process;

end rtl;