TOP_SYSTEM 1 TB
library ieee;
use ieee.std_logic_1164.all;

entity top_system1_tb is
end entity top_system1_tb;

architecture top_system1 of top_system1_tb is

  signal CLK : std_logic := '0';
  signal RST : std_logic := '1';
  signal ASTRB : std_logic := '1';
  signal DSTRB : std_logic := '1';
  signal DATA : std_logic_vector(7 downto 0);
  signal PWRITE : std_logic := '1';
  signal PWAIT : std_logic;
  signal SWITCHES_I : std_logic_vector(7 downto 0) := x"30";
  signal PSH_BUTTON : std_logic := '0';
  signal LEDS_O : std_logic_vector (7 downto 0);

begin -- architecture top_system1

  DUT: entity work.top_system1
    port map (
      CLK => CLK,
      RST => RST,
      ASTRB => ASTRB,
      DSTRB => DSTRB,
      DATA => DATA,
      PWRITE => PWRITE,
      PWAIT => PWAIT,
      SWITCHES_I => SWITCHES_I,
      PSH_BUTTON => PSH_BUTTON,
      LEDS_O => LEDS_O);

epp: entity work.epp_device
    port map (
  DATA => DATA,
PWRITE => PWRITE,
DSTRB => DSTRB,
ASTRB => ASTRB,
PWAIT => PWAIT);

  PSH_BUTTON <= not PSH_BUTTON after 1000 ns;
  CLK <= not CLK after 5 ns;
  RST <= '1', '0' after 25 ns;

end architecture top_system1;