PLANTILLAS EXAMEN

CABECERA BASICA
library ieee;
use ieee.std_logic_1164.all;

entity X is
    port(signals
);
end X;

architecture Y of X is
aux signals
begin

process (sensebility list)
variables
begin
codigo
end process;

end Y;
DECLARACION ARQUITECTURA
architecture <arch_name> of <entity_name> is
   -- declarative_items (signal declarations, component declarations, etc.)
begin
   -- architecture body
end <arch_name>;

DECLARACION COMPONENTES (87)
component <component_name>
generic (
   <generic_name> : <type> := <value>;
   <other generics>...
);
port (
   <port_name> : <mode> <type>;
   <other ports>...
);
end component;

INSTANCIACION COMPONENTES (87 Y 93)
<instance_name> : <component_name>
generic map (
   <generic_name> => <value>,
   <other generics>...
)
port map (
   <port_name> => <signal_name>,
   <other ports>...
);

CONVERSION INTEGER TO UNSIGNED
<unsigned_sig> = TO_UNSIGNED(<int_sig>, <integer_size>);

CONVERSION UNSIGNED TO INTEGER
<int_sig> = TO_INTEGER(<unsigned_sig>);

TIPOS DE DATOS
STD_LOGIC --'U','X','0','1','Z','W','L','H','-'
STD_LOGIC_VECTOR --Natural Range of STD_LOGIC
BOOLEAN --True or False
INTEGER --32 or 64 bits
NATURAL --Integers >= 0
POSITIVE --Integers > 0
REAL --Floating-point
BIT --'0','1'
BIT_VECTOR(Natural) --Array of bits
CHARACTER --7-bit ASCII
STRING(POSITIVE) --Array of characters
TIME --hr, min, sec, ms, us, ns, ps, fs
DELAY_LENGTH --Time >= 0
BUCLE FOR
for <variable_name> in <lower_limit> to <upper_limit> loop
   <statement>;
   <statement>;
end loop;

BULCE WHILE
while <condition> loop
   <statement>;
   <statement>;
end loop;

PROCESO COMBINACIONAL
process (<all_input_signals_seperated_by_commas>)
begin
   <statements>;
end process;

PROCESO ASYNC&SYNC CON CE
process (<clock>,<reset>)
begin
   if <reset> = '0' then
      <statements>;
   elsif (<clock>'event and <clock> = '1') then
      if <clock_enable> = '1' then
        <statements>;
      end if;
   end if;
end process;

CONSTANTES VARIABLES SEÑAL
constant <name>: <type> := <value>;
variable <name>: <type> := <value>;
signal <name>: <type> := <value>;

ACUMULADOR
    process (CLK)
    begin
        if (CLK'event and CLK='1') then
        if (CLR='1') then
        tmp <= "0000";
        else
        tmp <= tmp + D;
        end if;
        end if;
    end process;

    Q <= tmp;

PUERTA LOGICAS
<output> <= <input1> and <input2>;
<output> <= not <input1>;
<output> <= <input1> nand <input2> ;
<output> <= <input1> nor <input2> ;
<output> <= <input1> or <input2> ;
<output> <= <input1> xnor <input2> ;
<output> <= <input1> xor <input2> ;

COMPARADORES
CMP <= '1' when A >= B else '0';
CMP <= '1' when B >= A else '0';
CMP <= '1' when A == B else '0';
CMP <= '1' when B > A else '0';
CMP <= '1' when A > B else '0';

CONTADOR
 process (CLK)
    begin
        if (CLK'event and CLK='1') then
        if (CLR='1') then
        tmp <= "0000";
        else
        tmp <= tmp + 1;
        end if;
        end if;
    end process;

    Q <= tmp;

DECODIFICADOR O DEMULTIPLEXOR
process(<clock>)
begin
   if ( <clock>'event and <clock> ='1') then
      if ( <reset> = '1') then
        <output> <= "0000";
      else
        case <input> is
        when "00" => <output> <= "0001";
        when "01" => <output> <= "0010";
        when "10" => <output> <= "0100";
        when "11" => <output> <= "1000";
        when others => <output> <= "0000";
        end case;
      end if;
   end if;
end process;

CODIFICADOR O MULTIPLEXOR
process(<clock>)
begin
   if ( <clock>'event and <clock> ='1') then
      if ( <reset> = '1') then
        <output> <= "000";
      else
        case <input> is
        when "00000001" => <output> <= "000";
        when "00000010" => <output> <= "001";
        when "00000100" => <output> <= "010";
        when "00001000" => <output> <= "011";
        when "00010000" => <output> <= "100";
        when "00100000" => <output> <= "101";
        when "01000000" => <output> <= "110";
        when "10000000" => <output> <= "111";
        when others => <output> <= "000";
        end case;
      end if;
   end if;
end process;

BIESTABLE D CON CE
process (<clock>, <reset>)
begin
   if <reset>='1' then
      <output> <= '0';
   elsif (<clock>'event and <clock>='1') then
      if <clock_enable> = '1' then
        <output> <= <input>;
      end if;
   end if;
end process;

BIESTABLE T CON CE
process (<clock>, <reset>)
begin
   if <reset>='1' then
      <output> <= '0';
   elsif (<clock>'event and <clock>='1') then
      if <clock_enable> = '1' then
        <output> <= not(<output>);
      end if;
   end if;
end process;

LOGICAL SHIFTERS sll/srl
process(<clock>)
begin
   if ( <clock>'event and <clock> ='1') then
      case <selector> is
        when "00" => <output> <= <input> ;
        when "01" => <output> <= <input> sll/srl 1;
        when "10" => <output> <= <input> sll/srl 2;
        when "11" => <output> <= <input> sll/srl 3;
        when others => <output> <= <input> ;
      end case;
   end if;
end process;

 ARITMETIC SHIFTER sla/sra
process(<clock>)
begin
   if ( <clock>'event and <clock> ='1') then
      case <selector> is
        when "00" => <output> <= <input> ;
        when "01" => <output> <= <input> sla/sra 1;
        when "10" => <output> <= <input> sla/sra 2;
        when "11" => <output> <= <input> sla/sra 3;
        when others => <output> <= <input> ;
      end case;
   end if;
end process;

TRIESTATE
process (<enable>, <input>)
begin
   if (<enable>='1') then
      <output> <= <input>;
   else
      <output> <= 'Z';
   end if;
end process;
O

<output> <= <input> when <enable> ='1' else 'Z';
CONDICIONALES

   case (<2-bit select>) is
      when "00" =>
        <statement>;
      when "01" =>
        <statement>;
      when "10" =>
        <statement>;
      when "11" =>
        <statement>;
      when others =>
        <statement>;
   end case;

 if <condition> then
      <statement>
   elsif <condition> then
      <statement>
   else
      <statement>
   end if;

with <choice_expression> select
      <name> <= <expression> when <choices>,
        <expression> when <choices>,
        <expression> when others;

 <name> <= <expression> when <condition> else
        <expression> when <condition> else
        <expression>;